## Slide 1: Intelligent Threat Analysis and Surveillance System Using Multi-Module AI Fusion
Batch ID : ECE002
Akash S - CB.EN.U4ECE23202
Harish Venkat - CB.EN.U4ECE23219
Krithash V - CB.EN.U4ECE232058
Faculty Mentor : Anila Satheesh B

## Slide 2
Agenda
01 Motivation
02 Objective
03 Milestones / Deliverables
04 Novelty / Contribution
05 Methodology
06 Dataset
07 Model Selection
08 Results
09 Literature Survey
10 Research Gap

## Slide 3
Motivation
“Manual CCTV monitoring is too slow to stop an active threat.”
01
Conventional CCTV systems rely on continuous human monitoring, making them prone to delayed responses and missed security threats.
02
There is a growing demand for intelligent surveillance capable of automatically detecting weapons, tracking individuals, and assessing threats in real time.
03
Integrating AI with surveillance transforms passive CCTV infrastructure into an intelligent, automated system that improves response time and reduces manual effort.

## Slide 4
Objectives
• Detect persons and weapons (guns and knives) in real-time video streams, and perform robust multi-person tracking with stable identity assignment across consecutive frames. • Re-identify individuals who leave and later re-enter the camera's field of view, preserving their identity and threat history throughout the surveillance session.
• Estimate human pose to detect arm-raised behaviour and accurately associate detected weapons with the corresponding individuals using spatial and pose- based analysis. • Assess the threat level of each tracked individual based on weapon presence and behavioural cues, and automatically generate alerts, record evidence, and log security events for post-incident analysis.

## Slide 5
Milestones / Deliverables
Jun – Jul 2026
AI Detection Pipeline Development
YOLOv8 person & DeepSORT + OSNet re-identification integrated; persistent identity across occlusions achieved ; real-time pipeline optimized.
Aug – Sep 2026
Tracking & Identity Management
weapon detection integrated; custom dataset trained, weapon-person association,
Oct – Nov 2026
Threat Intelligence & Decision Engine
Pose estimation and hysteresis-based Threat State Machine developed.
Dec 2026 – Jan 2027
System Integration & Validation
All modules unified; alert management (logging, screenshots, recording) implemented and validated.
Feb – Mar 2027
Research Dissemination & Closure
Benchmarking, final research paper, documentation, and project report submission completed.

## Slide 6
Novelty / Contribution
01 Multi-Module AI Fusion
Combines weapon detection, tracking, Re-ID, and pose estimation into one real-time pipeline — systems-level innovation, not just a single algorithm.
02 Threat Analysis, Not Just Detection
Goes beyond “is there a weapon?” to assess who is carrying it, their behaviour, and an overall threat level.
03 Persistent Identity via Re-ID
Reconnects a tracked individual after temporary disappearance or re-entry using OSNet-based gallery matching.
04 Score Fusion
Combines embedding similarity with body aspect ratio to reduce false matches when people wear similar clothing.
05 Modular Architecture
Detector and tracker modules (e.g., YOLO, ByteTrack) can be upgraded or swapped without redesigning the system.
06 Practical Real-Time Design
Built for real-time operation on standard-GPU, CCTV-ready hardware, rather than offline high-end-GPU benchmarks.
07 Intelligent Alert Generation
Fuses weapon, pose, identity, and tracking history into a threat level before generating an alert — a decision-support system.
08 Designed for Future Expansion
Architecture already supports multi-camera input, cross-camera Re-ID, edge deployment, and audio event detection.

## Slide 7
Methodology
1. Video Acquisition Captures real-time frames from a CCTV camera or webcam and forwards each frame to the AI inference pipeline.
2. Person & Weapon Detection Two YOLOv8 models detect persons and weapons (guns, knives) in each frame, generating bounding boxes, class labels, and confidence scores.
3. Multi-Object Tracking & Re-Identification DeepSORT (Kalman Filter + Hungarian Algorithm, MobileNetv2) maintains identity across frames; OSNet re-identifies individuals who leave and re-enter the scene.
4. Pose Estimation MediaPipe Pose extracts wrist, elbow, shoulder, and hip landmarks to support behavioural analysis and weapon-person association.
5. Weapon-Person Association A three-stage geometric approach - wrist proximity, containment fraction, and IoU-based matching - assigns each weapon to the correct individual.
6. Threat Assessment A rule-based Threat State Machine classifies each individual as SAFE, CAUTION, HIGH or CRITICAL with hysteresis to prevent unstable fluctuations.
7. Alert Generation Visual overlays, audio alarms, event logging, screenshots, and incident recording are triggered based on the assessed threat level.

## Slide 9
Datasets
01 COCO val2017 — Detector Selection
2,693 images, 10,777 annotated person instances. The standard human-verified detection benchmark, used to rank YOLOv8s / YOLO11s / YOLO26s on the person class.
02 Market-1501 — Embedder Selection
1,501 identities, 32,668 crops, 6 campus cameras. First source with true identity labels; its cross-camera protocol mirrors “walked out and came back.”
03 MSMT17 — Cross-Domain Validation
4,101 identities, 126,441 crops, 15 cameras, indoor/outdoor, day/night. Tests transfer to a domain neither weight set has seen — governs the deployed weights.
04 MOT17 — Tracking & Occlusion
Full-frame surveillance video with per-frame identity ground truth. The only source that tests the tracker itself — motion, occlusion, entries and exits.
05 Own Recorded Clips — Deployment Evidence
Filmed on the actual deployment camera with tools/capture.py. Public benchmarks prove the software; only this footage proves the deployment works.

## Slide 10
Model Selection — Detector
Model | mAP50-95 | Recall | Params | Speed @640 (ms)
YOLOv8s | 0.5701 | 0.6964 | 11.17 M | 7.40
YOLO11s | 0.5821 | 0.7127 | 9.46 M | 9.18
YOLO26s (selected) | 0.5963 | 0.7130 | 10.01 M | 9.68
Selected: YOLO26s — best accuracy and recall on every metric, with fewer parameters than YOLOv8s. Run at imgsz=640 to match the native 640×480 camera; higher resolutions cost 30–64% more time for no larger person crops.

## Slide 11
Model Selection — Re-ID Embedder
Embedder | Dim | Rank-1 | mAP | ms / img
OSNet x1_0 (MSMT17 — deployed) | 512 | 57.2% | 30.4% | 0.75
OSNet x1_0 (Market-1501) | 512 | 94.3% | 83.6% | 1.56
OSNet x1_0 (ImageNet) | 512 | 14.5% | 4.5% | 0.64
MobileNetV3-Small | 576 | 11.5% | 3.5% | 0.47
MobileNetV3-Large | 960 | 9.8% | 2.6% | 0.68
MobileNetV2 | 1280 | 6.8% | 2.2% | 0.88
Selected: OSNet, MSMT17 weights. MobileNetV2/V3 are ImageNet classifiers repurposed for tracking, not re-ID models — OSNet is ~12× more accurate at telling two people apart (30.4% vs 2.2% mAP) at comparable speed and a smaller embedding. The base project used MobileNetV2 inside its tracker — effectively matching identity with a model that scores 2.2% mAP at distinguishing people.

## Slide 12
Tracking Algorithm — DeepSORT
1. Kalman Filter Predict — constant-velocity 8-D state (position, aspect ratio, height + velocities); predicts every track's position this frame.
2. Mahalanobis Gating — a χ² threshold (9.4877, 4 DOF) rejects detection-track pairs that are physically impossible, before matching is attempted.
3. Cosine Appearance Metric — the injected 512-d OSNet embedding is compared at a calibrated max-distance of 0.3735.
4. Hungarian Assignment — scipy's linear_sum_assignment solves the full cost matrix optimally, not greedily, so two tracks can never both claim one detection.
5. Matching Cascade — recently-seen tracks get first claim on a detection, so a fresh track doesn't lose out to one that has been stale for several frames.
6. IoU Fallback — for unconfirmed or just-lost tracks, a looser IoU-based match (≤ 0.7) catches cases appearance alone misses.
7. Track State Machine — Tentative → Confirmed (after 3 consecutive matched frames) → Deleted (after 5 consecutive missed frames).
One embedding, two jobs: the same OSNet feature drives both this frame-to-frame match (DeepSORT) and the long-term identity gallery (next slide) — sharing one representation instead of two is what fixed the base project's identity-swap bug.

## Slide 13
Re-ID Gallery — Identity & Storage
Property | Value
Representation | 512-d OSNet embedding, L2-normalised
Samples stored per identity | 16, diversity-selected (replaces the most redundant sample, not FIFO)
Storage size per identity | ~41.4 KB (measured)
Storage location | RAM only — no disk, no database
Active-identity lifetime | Never expires while currently tracked
Dormant-identity lifetime | Expires 600 s (10 min) after last seen
Gallery capacity | 100 identities; LRU-evicts oldest dormant entries beyond that (~4.0 MB at capacity)
Admission gate (what gets stored) | Crop height ≥ 64 px, confidence ≥ 0.5, not side-clipped, ≥ 5 pose keypoints (soft)
Match decision | MATCHED ≥ 0.7327 (margin ≥ 0.0957) · NEW < 0.5617 · else PROVISIONAL (deferred ≤ 30 frames)

## Slide 14
Re-ID Gallery — Capacity & Frame Cost
People in frame | Embed cost (ms) | Total / frame (ms) | Budget used (33 ms) | Ceiling FPS
1 | 3.24 | 12.74 | 38% | 79
8 | 3.81 | 13.31 | 40% | 75
16 | 7.78 | 17.28 | 52% | 58
24 | 11.36 | 20.86 | 63% | 48
32 | 15.10 | 24.60 | 74% | 41
Cost is a step function, not linear — the CUDA graph batches 8 embeddings at a time, so 1–8 people cost almost the same, and each additional block of 8 adds ~3.8 ms. The system stays above the 30 FPS real-time target with up to at least 32 simultaneous people. In practice the limit in crowded scenes is detector recall, not identity — on MOT17, tracking accuracy (IDF1) tracks detection recall almost exactly, so the detector loses people before identity ever becomes the bottleneck.

## Slide 15
Validation Scenarios
# | Scenario | People | Purpose | Status
1 | Short re-entry (5 s gaps) | 1 | Core re-entry accuracy test | Recorded
2 | Medium re-entry (30 s gaps) | 1 | Validates the 600 s dormant-identity TTL | Pending
3 | Re-entry with appearance change | 1 | Jacket / bag — hardest solo case | Pending
4 | Occlusion without leaving | 1 | Pillar / doorway passes | Pending
5 | Distance sweep | 1 | Sets the minimum crop-height for admission | Pending
6 | Empty scene / ghost check | 0 | True-negative pass criterion | Recorded
7 | Same re-entry, no backlight | 1 | Lighting A/B (backlit vs. even) | Recorded
8 | Camera high, angled down | 1 | Real CCTV viewpoint | Pending
9 | Sitting, crouching, turning | 1 | Pose variation | Pending
10 | Two people crossing | 2 | ID swaps, false merges, threshold calibration | Recorded
11 | Similar clothing | 2 | Hardest case — appearance collapse | Pending
Recorded scenarios produced every number on the next slide: #1 & #7 → re-entry accuracy and lighting sensitivity; #6 → the true-negative / ghost-box test; #10 → the multi-person crossing test. Remaining scenarios are planned alongside the Aug–Sep 2026 milestone.

## Slide 16
Results — Key Numbers
Metric | Result
Real-time speed | 35.8 FPS end-to-end (23.9 FPS with pose) — RTX 5070 Laptop
Re-ID implementation | Reproduces published Market-1501 / MSMT17 benchmarks within 1%
Tracking (MOT17-09) | IDF1 84.1%, MOTA 67.7%, 0 ID switches
Re-ID on deployment camera | 100% (8/8 re-entries), 0 false merges, 0 false splits
Multi-person crossing | 3 identities for 2 people (1 false split), 0 duplicate-id frames
Ghost-box false positives (empty room) | 0.44% (901-frame true-negative test), 0 identities created
Capacity | Sustains ≥30 FPS with up to 32 people in frame
Threshold calibration | Separability 0.2135; 77.1% re-entry recall @ 1% false-merge budget
Unit tests | 22/22 passing

## Slide 17
Evidence — Single-Person Re-Identification

## Slide 18
Evidence — Multi-Person Entry / Exit

## Slide 19
Evidence — Multi-Person Simultaneous Re-Identification

## Slide 20: Literature Survey
S.No | Title of the Paper | Publication & Year | Methodology | Limitations | Inferences
1 | A Multi-Attention Approach for Person Re-Identification Using Deep Learning | Sensors (MDPI), 2023 | Proposes a multi-attention person Re-ID framework combining a Position Attention Module (PAM) and Efficient Channel Attention (ECA) within a multi-part feature network to jointly learn spatial, channel, and contextual features. Evaluated on Market-1501, DukeMTMC-reID, and CUHK03, reaching up to 95.93% Rank-1 (96.41% after re-ranking). | Targets person Re-ID only, not full surveillance (no detection, tracking, or threat analysis). Depends on accurate person detection and large annotated datasets, and adds computational overhead that can limit edge deployment; performance still degrades under severe occlusion or poor illumination. | Shows that combining spatial (PAM) and channel (ECA) attention significantly improves discriminative Re-ID features and robustness to appearance variation, reinforcing attention mechanisms as valuable for multi-camera person tracking in intelligent surveillance.
2 | AI-Based Weapon Detection for Security Surveillance: Recent Research Advances (2016–2025) | Electronics (MDPI), 2025 | PRISMA-based systematic review of 101 papers (2016–2025) comparing ML, CNN, Faster R-CNN, SSD, YOLO (v1–v12), Transformer, and hybrid models for weapon detection across image, video, infrared, X-ray, and multimodal inputs, benchmarked on Precision, Recall, F1-score, and mAP for real-time surveillance and smart-city deployment. | As a review, it proposes no new model and its conclusions inherit inconsistencies from the surveyed studies (differing datasets/metrics). Identifies unresolved challenges: dataset variability, lack of standardized benchmarks, occlusion, poor illumination, small-object detection, privacy, and compute cost. | Concludes YOLOv5–YOLOv8 offer the best speed/accuracy trade-off for real-time detection while Faster/Mask R-CNN favor localization accuracy; calls for standardized datasets, lightweight edge models, and real-world validation.
3 | BlazePose GHUM Holistic: Real-time 3D Human Landmarks and Pose Estimation | arXiv, 2022 (Google Research) | Lightweight real-time 3D human pose framework combining BlazePose body-landmark detection, a hand re-crop/landmark module, and a GHUM statistical body model; predicts 33 body + 21×2 hand landmarks via a detector-tracker pipeline, with an MLP-Mixer-based GHUM Lifter converting landmarks to pose/shape. Runs at ~15 FPS on mobile. | Focused solely on pose estimation — no detection, tracking, or activity recognition. Accuracy depends on clear body visibility and degrades under heavy occlusion, extreme viewpoints, or overlapping people; facial expression modeling remains limited. | Demonstrates that accurate on-device 3D pose estimation from a single RGB camera is practical in real time, establishing a strong basis for pose-driven behaviour-analysis modules within intelligent surveillance systems such as ours.

## Slide 21
S.No | Title of the Paper | Publication & Year | Methodology | Limitations | Inferences
4 | Body Part-Based Representation Learning for Occluded Person Re-Identification | arXiv, 2022 | Proposes BPBreID for occluded person Re-ID using body-part attention, GiLt training, visibility-aware part matching, and holistic plus local feature learning. Evaluated on Market-1501, DukeMTMC-ReID, Occluded-Duke, Occluded-ReID, and P-DukeMTMC, achieving state-of-the-art performance under heavy occlusion. | Focuses only on person Re-ID and requires accurate human parsing. Does not include detection, tracking, behaviour analysis, or threat assessment. Performance decreases with severe occlusion or poor body-part localization. | Demonstrates that body-part attention and visibility-aware matching significantly improve Re-ID under occlusion. Highlights the importance of local body features for robust surveillance applications.
5 | ByteTrack: Multi-Object Tracking by Associating Every Detection Box | arXiv, 2022 | Introduces the BYTE association algorithm that retains both high- and low-confidence detections for tracking. Uses Kalman Filter prediction, IoU/Re-ID matching, Hungarian Algorithm, and two-stage association to recover occluded targets. Evaluated on MOT17, MOT20, HiEve, and BDD100K with state-of-the-art real-time performance. | Focuses only on multi-object tracking and depends on an external detector. Does not perform Re-ID across cameras, weapon detection, pose estimation, behaviour analysis, or threat assessment. | Shows that associating low-confidence detections greatly improves tracking continuity and reduces identity fragmentation while maintaining real-time performance.
6 | Development and Optimization of Deep Learning Models for Weapon Detection in Surveillance Videos | Applied Sciences (MDPI), 2022 | Develops a real-time weapon detector using Scaled-YOLOv4, custom weapon datasets, extensive preprocessing, hyperparameter optimization, and TensorRT acceleration for Jetson Nano deployment. Achieves 92.1% mAP and high inference speed. | Limited to weapon detection and lacks tracking, person Re-ID, behaviour analysis, and threat assessment. Cannot identify the person carrying the weapon or preserve identity across frames. | Demonstrates that Scaled-YOLOv4 with TensorRT enables accurate and efficient edge-based weapon detection suitable for real-time surveillance.

## Slide 22
S.No | Title of the Paper | Publication & Year | Methodology | Limitations | Inferences
7 | Distributed Intelligent Video Surveillance for Early Armed Robbery Detection based on Deep Learning | IEEE, 2024 | Presents a distributed edge-cloud surveillance system using YOLOv5s for weapon detection, TensorRT optimization, Momentum confidence accumulation, and 3DCNN for robbery verification. Integrates IoT, PostgreSQL, Android, and WhatsApp alerts. | Does not perform tracking, person Re-ID, or identity persistence. Knife detection remains challenging, and cloud communication introduces latency. | Demonstrates that combining edge intelligence with cloud verification improves robbery detection while reducing false positives in surveillance systems.
8 | Human Pose Estimation Using MediaPipe Pose and Optimization Method Based on a Humanoid Model | Applied Sciences (MDPI), 2023 | Combines MediaPipe Pose with a humanoid kinematic model and uDEAS optimization to estimate accurate 3D human poses. Uses joint constraints and center-of-mass optimization for realistic posture reconstruction on low-cost hardware. | Supports only single-person pose estimation and depends on accurate landmark detection. Does not include detection, tracking, Re-ID, or surveillance intelligence. | Demonstrates that optimization-based pose estimation can achieve accurate real-time 3D pose reconstruction without GPU acceleration.
9 | Tran-GCN: A Transformer-Enhanced Graph Convolutional Network for Person Re-Identification in Monitoring Videos | IET Computer Vision, 2025 | Combines OpenPose, ResNet-50, Transformer, and Graph Convolution Networks for robust person Re-ID. Uses pose features, local appearance, and global context with Triplet and Contrastive losses. Evaluated on Market-1501, DukeMTMC-ReID, and MSMT17. | Computationally expensive and requires large labelled datasets. Focuses only on Re-ID without detection, tracking, weapon detection, or threat analysis. | Demonstrates that combining pose, CNNs, Transformers, and GCNs significantly improves Re-ID robustness against pose variation and occlusion.

## Slide 23
S.No | Title of the Paper | Publication & Year | Methodology | Limitations | Inferences
10 | Improving Handgun Detection Through a Combination of Visual Features and Body Pose-Based Data | Pattern Recognition (Elsevier), 2023 | Combines OpenPose body keypoints with CNN and Vision Transformer-based visual features for handgun detection. Uses feature fusion and false-positive filtering to improve recognition under challenging CCTV conditions. | Depends heavily on accurate pose estimation and processes only individual images. Does not support tracking, Re-ID, behaviour analysis, or intelligent surveillance. | Shows that integrating body pose with visual appearance significantly improves handgun detection accuracy in surveillance imagery.
11 | Multi-scale and Attention Enhanced Graph Convolution Network for Skeleton-Based Violence Action Recognition | Frontiers in Neurorobotics, 2022 | Proposes MSA-STGCN using multi-scale graph convolutions, SE attention, hybrid dilated convolutions, and four-stream skeleton representations for violence recognition. Evaluated on NTU RGB+D and Kinetics Skeleton datasets. | Depends on accurate skeleton extraction and recognizes only predefined violence actions. Does not include detection, tracking, Re-ID, or weapon recognition. | Demonstrates that attention-enhanced graph convolution effectively models spatial-temporal skeleton information for violence recognition.
12 | Real-Time Weapon Detection Using YOLOv8 for Enhanced Safety | arXiv, 2024 | Implements a YOLOv8-based weapon detection framework using GAN-augmented datasets, data augmentation, FPN, and NMS for real-time surveillance. Achieves strong Precision, Recall, F1-score, and mAP performance. | Performs only weapon detection and lacks tracking, Re-ID, behaviour analysis, threat scoring, and identity management. | Confirms YOLOv8 as an effective real-time detector but highlights the need for additional surveillance intelligence modules.

## Slide 24
S.No | Title of the Paper | Publication & Year | Methodology | Limitations | Inferences
13 | StrongSORT: Make DeepSORT Great Again | arXiv, 2023 | Enhances DeepSORT using YOLOX-X, BoT Re-ID embeddings, EMA, ECC camera compensation, NSA Kalman Filter, AFLink, and GSI trajectory interpolation to improve multi-object tracking accuracy. | Focuses solely on tracking and assumes object detection is already available. Does not perform weapon detection, pose estimation, Re-ID across surveillance sessions, or threat analysis. | Demonstrates that enhanced association strategies significantly reduce identity switches and improve tracking robustness while maintaining real-time performance.
14 | Tiny Asymmetric Feature Normalized Network for Person Re-Identification System | IEEE Access, 2022 | Proposes TAFN-Net using BIG normalization, IBLR SE blocks, non-local attention, random erasing, and Triplet plus Cross-Entropy losses to generate lightweight yet robust Re-ID embeddings. Evaluated on Market-1501, DukeMTMC-ReID, and GPP-ReID. | Limited to person Re-ID and does not include detection, tracking, behaviour analysis, or intelligent surveillance capabilities. | Demonstrates that advanced normalization strategies enable lightweight models to achieve competitive Re-ID accuracy with low computational cost.
15 | Weapon Detection with FMR-CNN and YOLOv8 for Enhanced Crime Prevention and Security | Scientific Reports (Nature Portfolio), 2025 | Introduces the FMR-CNN surveillance framework combining Faster R-CNN, Mask R-CNN, YOLOv8, MobileNetV3, and MobileNetV2 for weapon detection, segmentation, behaviour assessment, and automated API-based alert generation. Achieves 98.7% accuracy and 90.1% mAP. | Does not perform person Re-ID, identity persistence, pose estimation, or weapon ownership identification. Computational complexity is high due to multiple deep models. | Demonstrates that hybrid detection and segmentation significantly improve surveillance accuracy, but additional identity management is required for intelligent surveillance.

## Slide 25
S.No | Title of the Paper | Publication & Year | Methodology | Limitations | Inferences
16 | Weapon Operating Pose Detection and Suspicious Human Activity Classification Using Skeleton Graphs | Mathematical Biosciences and Engineering, 2023 | Uses VGG-19 skeleton extraction, DeepSORT tracking, LSTM-RNN temporal modelling, ADAM optimization, and Kalman filtering to classify eight suspicious human activities from skeleton graphs. Generates real-time alarms for activities such as shooting, crawling, throwing, and weapon operation. | Does not explicitly detect weapons and relies on body posture. Lacks person Re-ID, multi-camera identity management, weapon ownership identification, threat scoring, evidence logging, and long-term identity preservation. | Demonstrates that combining skeleton graphs with DeepSORT and LSTM effectively recognizes suspicious activities, but remains primarily an activity recognition framework rather than a complete intelligent surveillance system.
17 | Weapon Detection in Surveillance Videos Using YOLOv8 and PELSF-DCNN | E3S Web of Conferences (ICMED-ICMPC), 2023 | Proposes a hybrid framework combining YOLOv8, Wiener Filtering, PDFMSR preprocessing, Diamond Search motion estimation, handcrafted feature extraction, CSBO optimization, and the PELSF-DCNN classifier for weapon detection. Achieves 97.5% accuracy and 95.42% mAP. | Limited to weapon detection and lacks tracking, person Re-ID, pose estimation, behaviour analysis, threat assessment, and multi-camera surveillance support. The pipeline is computationally complex due to multiple preprocessing and optimization stages. | Demonstrates that combining advanced preprocessing, handcrafted features, optimization algorithms, and YOLOv8 significantly improves weapon detection accuracy, but additional modules are required for complete intelligent surveillance.

## Slide 26
Research Gap & How We Close It
01 Weapon detected, but ownership isn't
Detection-only or hand-patch-classification systems [6,10,12,15,17] never bind a weapon to a specific tracked person. Our counter: a 3-stage association cascade — wrist proximity (≤60px) → containment (≥0.30) → IoU fallback (≥0.20).
02 Identity resets after occlusion
ByteTrack, StrongSORT and skeleton-based systems [5,13,15,16] lose identity — and threat history — the moment someone leaves the frame. Our counter: an OSNet Re-ID gallery (512-d, cosine ≥0.65, fused with body-ratio, 300s memory) restores it on reappearance.
03 Siloed, single-task pipelines
Detection-only, tracking-only or Re-ID-only work [1,3,4,5,6,8,9,11,12,13,14,17] never combines with the others — including a 2024 distributed edge+cloud design (7) that still cannot identify individuals and runs at only 4.43 FPS. Our counter: one real-time loop — detection → tracking → Re-ID → pose → association → threat FSM → alert.
04 Threat output is binary, not graded
FMR-CNN and skeleton-action systems [15,16] output a single coarse trigger or a “normal vs suspicious” label — no per-person severity. Our counter: a 4-level threat FSM (SAFE → CAUTION → HIGH → CRITICAL) with a 45-frame hysteresis lock, so alerts escalate instantly but never flicker.
05 Heavy pipelines don't hold real time
Multi-branch or multi-stage stacks [9,15,17] pay in heavy GPU cost or ≈ 9 FPS; the distributed edge design (7) manages only 4.43 FPS. Our counter: a single-stage YOLOv8s stack with interval scheduling (weapon /3, pose /4, Re-ID /15 frames) sustains ≈30 FPS GPU / ≈10 FPS CPU.
06 Bottom line
17 papers reviewed — including a 101-paper systematic review (2) that independently confirms the field-wide gap — each solve one task in isolation. Ours is the only system that detects a weapon, identifies who holds it, remembers them across occlusion, and grades the threat, in one real-time loop.

## Slide 27
Research Gap — Reference Papers
# | Paper | Venue, Year
1 | A Multi-Attention Approach for Person Re-Identification Using Deep Learning | Sensors (MDPI), 2023
2 | AI-Based Weapon Detection for Security Surveillance: Recent Research Advances (2016–2025) | Electronics (MDPI), 2025
3 | BlazePose GHUM Holistic: Real-time 3D Human Landmarks and Pose Estimation | arXiv, 2022
4 | Body Part-Based Representation Learning for Occluded Person Re-Identification | arXiv, 2022
5 | ByteTrack: Multi-Object Tracking by Associating Every Detection Box | arXiv, 2022
6 | Development and Optimization of Deep Learning Models for Weapon Detection in Surveillance Videos | Applied Sciences (MDPI), 2022
7 | Distributed Intelligent Video Surveillance for Early Armed Robbery Detection based on Deep Learning | IEEE, 2024
8 | Human Pose Estimation Using MediaPipe Pose and Optimization Method Based on a Humanoid Model | Applied Sciences (MDPI), 2023
9 | Tran-GCN: A Transformer-Enhanced Graph Convolutional Network for Person Re-Identification in Monitoring Videos | IET Computer Vision, 2025
10 | Improving Handgun Detection Through a Combination of Visual Features and Body Pose-Based Data | Pattern Recognition (Elsevier), 2023
11 | Multi-scale and Attention Enhanced Graph Convolution Network for Skeleton-Based Violence Action Recognition | Frontiers in Neurorobotics, 2022
12 | Real-Time Weapon Detection Using YOLOv8 for Enhanced Safety | arXiv, 2024
13 | StrongSORT: Make DeepSORT Great Again | arXiv, 2023
14 | Tiny Asymmetric Feature Normalized Network for Person Re-Identification System | IEEE Access, 2022
15 | Weapon Detection with FMR-CNN and YOLOv8 for Enhanced Crime Prevention and Security | Scientific Reports (Nature), 2025
16 | Weapon Operating Pose Detection and Suspicious Human Activity Classification Using Skeleton Graphs | Math. Biosciences & Engineering, 2023
17 | Weapon Detection in Surveillance Videos Using YOLOv8 and PELSF-DCNN | E3S Web of Conferences, 2023

## Slide 28
References
[1] M. T. Bhatti, M. G. Khan, M. Aslam, and M. J. Fiaz, “Weapon Detection in Real-Time CCTV Videos Using Deep Learning,” IEEE Access, vol. 9, pp. 34366–34382, 2021, doi: 10.1109/ACCESS.2021.3059170.
[2] P. Shanthi and V. Manjula, “Weapon Detection with FMR-CNN and YOLOv8 for Enhanced Crime Prevention and Security,” Scientific Reports, vol. 15, 2025, doi: 10.1038/s41598-025-07782-0.
[3] K. Zhou, Y. Yang, A. Cavallaro, and T. Xiang, “Omni-Scale Feature Learning for Person Re-Identification,” Proc. IEEE/CVF International Conference on Computer Vision (ICCV), Seoul, South Korea, 2019, pp. 3702–3712, doi: 10.1109/ICCV.2019.00380.
[4] D. Berardini et al., “A Deep-Learning Framework Running on Edge Devices for Handgun and Knife Detection from Indoor Video-Surveillance Cameras,” Multimedia Tools and Applications, vol. 83, no. 7, pp. 19109–19127, 2024, doi: 10.1007/s11042-023-16231-x.
[5] T. Murugan et al., “AI-Based Weapon Detection for Security Surveillance: Recent Research Advances (2016–2025),” Electronics, vol. 14, no. 23, Art. 4609, 2025, doi: 10.3390/electronics14234609.
[6] P. Chaware, V. Dhamdhere, M. Sawane, S. Patil, P. Sarode, and K. Ukey, “Development of Intelligent Video Surveillance System Using Deep Learning and Convolutional Neural Networks: A Proactive Security Solution,” Engineering Proceedings, vol. 114, no. 1, Art. 11, 2025, doi: 10.3390/engproc2025114011.
[7] A. Thakur, A. Shrivastav, R. Sharma, T. Kumar, and K. Puri, “Real-Time Weapon Detection Using YOLOv8 for Enhanced Safety,” arXiv preprint arXiv:2410.19862, 2024.
[8] N. Wojke, A. Bewley, and D. Paulus, “Simple Online and Realtime Tracking with a Deep Association Metric,” Proc. IEEE International Conference on Image Processing (ICIP), Beijing, China, 2017, pp. 3645–3649, doi: 10.1109/ICIP.2017.8296962.
[9] S. Yan, Y. Xiong, and D. Lin, “Spatial Temporal Graph Convolutional Networks for Skeleton-Based Action Recognition,” Proc. AAAI Conference on Artificial Intelligence, New Orleans, LA, USA, 2018, pp. 7444–7452.
[10] J. Redmon, S. Divvala, R. Girshick, and A. Farhadi, “You Only Look Once: Unified, Real-Time Object Detection,” Proc. IEEE Conference on Computer Vision and Pattern Recognition (CVPR), Las Vegas, NV, USA, 2016, pp. 779–788.

## Slide 29
Thank You
Akash S • Harish Venkat • Krithash V